## Slide 1
Non-Inverting Op-Amp with Memristor Feedback
Figure 1 shows the circuit diagram of a non-inverting amplifier where the resistors R1 and R2 have been replaced by m1 and m2. Where the m1 and m2 are models of the HP memristor.
The HP memristor, as described in the introduction and tutorial is a memristor that is a device that can switch between a high and low resistance. Due to the memristors having opposite polarity when one memristor is at its Ron state the other memristor is at its Roff state.
The standard expression for the gain of a non-inverting amplifier is altered for memristor behaviour i.e.
This equation now has two possible values. If m2 is at Roff and m1 is at Ron the value of the the gain will be high. If m2 is at Ron and m1 is at Roff the gain will be only slightly above 1.
A positive input voltage will cause m2 to be at Roff and m1 to be at Ron. A negative input voltage will cause m1 to be at Roff and m2 to be at Ron. Therefore only the positive input receives a large gain.
Notes: apps_intro