## Slide 1
Memristor Based Phase Shift Oscillator
A standard phase shift oscillator has the resistor R1 in the feedback loop replace with a HP memristor. The memristor is operated in the soft switching
The following parameters of the classic BCM model were used for the memristor: (Ron, Roff, M(x(0)), D, μv, p) = (16 kΩ, 500 Ω, 6.5 kΩ, 10 nm, 10−13 m2V−1s−1, 10).
This type of oscillator has no input, it relies on an initial voltage on one or more of the capacitors. The op-amp used is an ideal infinite gain op amp.
As can be seen from the plot, when the output voltage is decreasing the memristor is at its Roff state. This causes the voltage to decrease at a relatively slow rate. When the output voltage switches and starts to increase the memristor switches to its Ron state. This causes the voltage to increase at a higher rate, than the decrease rate. As this rate is higher, the amount of time the memristor spends at its Ron is shorter then the Roff stage, before it switches state again. This results in the non-sinusoidal output from the oscillator, as shown.
Figure 1: Memristor-based Oscillator
Notes: apps_intro