## Slide 1
Programmable Circuits
The following 3 pages go through 3 different Programmable Memristor Circuit Types:
  Op-amps
  Oscillators
  Rectifiers & Converters
Each page includes:
  An explanation of the circuit
  A button at the top of the page to open the circuit in Simulink
Notes: apps_intro

## Slide 2
The memristor used to emulate the synapse is described by the equations
Where α and β characterise the rate of memristance change,
VT is a threshold voltage,
R1 and R2 are limiting values and
θ(.) is a step function which causes the memristor to be bound by the limits R1 and R2.
This memristor gives a zero pinched as shown in figure(3), with
Although much is unknown about neurons, some simple brain functions can be simulated using simplified structures. Where a neuron reacts to an input voltage. If the input voltage is above a certain threshold the neuron fires a positive voltage pulse in the forward direction and a negative voltage pulse in the negative direction. It then waits a period of time and repeats. As shown in figure(2), note Vout has been shifted for clarity
α = β = 146 kΩ V-1 s-1
R1 = 675 Ω
R2 = 10 kΩ
VT=4V
V = 2 sin(ft) V

## Slide 3
Simulink – Simscape
The neural network shown in figure(1) has been re-created using Simulink, Simscape and the created memristor model.
In this circuit the neurons have been created using MATLAB functions and have been reduced to subsystems for simplicity.
In the below graphs it is clear that at first the sound of a buzzer does not cause the dog to salivate and the sight of food does. When the buzzer is sounded along with the sight of the food, the resistance of the memristor clearly falls. This is due to the reverse firing of the neuron N3. When the food is seen N3 fires a negative pulse towards both N1 and N2. If there is a buzzer sounding when this happens i.e. if N2 is firing at the same time there is now a greater voltage drop across the synapse N2, this greater voltage drop allows the memristor reduce the value of its resistance.