## Slide 1
Square Wave to Saw tooth Wave Rectifier
In this circuit the memristors are operated so that the boundaries of the device are never hit (soft switching scenario). As the memristors have opposite polarity, when the memristance of one memristor is increasing the memristance of the other is decreasing and vice versa.
Essentially this circuit acts as a voltage divider. With reference to one period of the square wave input, as the input voltage goes positive the memristance of m2 increases linearly while the memristance of m1 decreases linearly. This causes the voltage drop Across m2 to increase linearly until the input voltage switches to its negative value. This switch, triggers an analogous positive-to-negative transition in the output voltage, and thereafter till the end of the period the memristance of m1 increases linearly while the memristance of m2 decreases linearly, resulting in a linear increase in the voltage drop across m2 from its negative value. This results in a sawtooth wave output for a square wave input.
These results were also recreated using a memristor defined by the equations:
dx/dt = sign(v) * k
v=ix
Where k is a constant. This memristor was used to show the availability of other memristors in the software package.
Figure 1: Square Wave to Saw tooth Wave Rectifier
Notes: apps_intro