## Slide 1
A memristor is a two terminal, passive circuit element
Two Terminals
1
2
Passive:
Does not require power to operate
A memristor behaves like a resistor with memory (an internal state)
Memory
+
=
The state of a memristor is the value of its resistance at a given point in time. An applied voltage can change this resistance, but if no voltage is applied the resistance remains constant. In this way a memristor has memory.
Notes: Intro_what

## Slide 2
Circuit Element | Equation | Function | Unit
Resistor |  |  | 
Capacitor |  | where | 
Inductor |  | where | 
Memristor |  |  | 
Circuit Element | Equation | Function | Unit
Resistor |  |  | 
Capacitor |  |  | 
Inductor |  |  | 
Memristor |  |  | 
There are four fundamental circuit variables:
voltage V
electric current I
electric charge q
magnetic flux 
There are three traditional passive circuit elements:
Resistor
Capacitor
Inductor
These are shown in the four corners of the figure below. Each variable has a fundamental relationship with each other variable, either through a resistor, capacitor, inductor or differential equations, as shown below. For the sake of completeness, there must also be a two-terminal circuit element which relates  and q. This element is a memristor and is inserted below.
“A memristor relates magnetic flux  and electric change q.”
Notes: intro_variable

## Slide 3
“A memristor relates magnetic flux  and electric change q.”
Both quantities are defined as follows:
A memristor may be either controlled by the charge through it or by the flux through it. Either a change in the charge or flux will change the internal state in the memristor. As above charge and flux have a clear relationship to voltage and current. Therefore a relationship between the voltage and current through a memristor can be developed. It is sufficient to begin with a charge controlled memristor.
The flux of a charge controlled memristor is a function of the charge (the state):
The known relationship between flux and voltage:
is simplified down by:
so:
where the memristance (in Ohms Ω) is defined as:
This definition is similar to Ohm’s law. In Ohm’s law the resistance is a constant, but for a memristor the memristance depends on the entire past history of the charge through the memristor from , i.e. the state depends on the history.
Notes: intro_qphi

## Slide 4
The previous page has shown how the flux and charge values of the memristor can be controlled with voltage and current. The charge controlled memristor is defined by a charge dependent Ohm’s Law:
The important point about this equation is knowing that the relationship between charge and current is:
This important as it allows us to generalise the memristor definition. The definition of the memristor requires both an equation defining the output and an equation defining the state. The state of the memristor is in this case is q, but will henceforth be generalised as x. Therefore the defining functions are:
In many cases, this ideal definition is not enough to encapsulate the entire behaviour of the memristor. A more precise definition is necessary for the general memristor. One important characteristic property of a memristor is that when (which will be explained further on the next page), so any waveform source must follow these constraints. This can be generalised by including the current (or input) in the memristor definition:
this is true for an
Ideal Memristor
this is a general
Memristor
Notes: Intro_geneqn

## Slide 5
The Pinched Hysteresis Loop is a very important characteristic of a memristor. The voltage of the memristor is plotted against its current. For a memristor driven by a sinusoidal current source the plot will always be a pinched hysteresis loop.
Pinched: when
Hysteresis: There is a delay between the maximum & minima of the input current and the voltage through the memristor causing the shape shown in the plot on the right.
At very high frequency the loop reduces to a straight line and the memristor becomes nothing more than a linear time-invariant resistor. At very low frequencies it becomes indistinguishable from a nonlinear resistor.
The Pinched Hysteresis Loop alone does not model a memristor. The loop cannot be used to predict the response of the system to an applied input (current or voltage). Therefore either a  – q curve or a memristance vs. state map is needed. A memristance vs. state map is shown on the right for . The state in this case is the charge, q.
[2]
[4]
Notes: intro_hysteresis

## Slide 6
Chua defined the memristor as the fourth fundamental circuit element, a device which relates  & q. [1]
1971
Chua & Kang generalise the 1971 memristor as part of a broader class of “memristive systems”. They also introduced the idea of a memristive device having a state variable. [2]
1976
Chua introduced a periodic table of all two-terminal circuit elements. [5]
2003
HP introduced their physical memristor.
[2]
2008
Di Ventra et al. expanded memristive systems to include the memcapacitor and meminductor. [6]
2009
Chua redefined the memristor as “all 2-terminal non-volatile memory devices based on resistance switching are memristors”. [4]
2011
2013
Notes: intro_timeline

## Slide 7
HP Crossbar Memristor Composition [3]
Pinched hysteresis loop and
“q vs. ” for the HP memristor [3]
The largest breakthrough in memristor development came when HP published a paper in 2008 entitled “The missing memristor found”1. Stanley Williams and his team had been working on developing a new high speed dense memory based on a crossbar array at the nanoscale. They needed a switch that could connect overlapping crossbars, the switch they needed was a memristor.
They developed the device by sandwiching a cube of between the platinum crossbars, as shown on the right. A region of the was auto doped by removing oxygen atoms creating a region. These positive oxygen deficiencies can drift through the entire cube and are moved by applying an electric current. This movement changes the resistance of the memristor. The dopants will also remain in their position until a current is applied again. In this way the memristor has memory.
Fig. a below shows the initial condition of the memristor. The oxygen vacancies act as positive dopants. In Fig. b a positive bias is applied to the memristor and the positive charges are repelled throughout the memristor causing the boundary between the two materials to shift. In this way the resistance of the device is lowered and the device is said to be on. In Fig. c a negative bias is applied, the positive charges are attracted to the top of the device, the resistance increases and the device is said to be off. [3]
Voltage through memristor:
RON = resistance when on, ROFF = resistance when off
D = length of device, w = width of doped region
Memristance:
= average ion mobility
State Equation:
Notes: intro_HP

## Slide 8
HP Crossbar Memristor Composition [3]
Pinched hysteresis loop and
“q vs. ” for the HP memristor [3]
HP Memristor
The largest breakthrough in memristor development came when HP published a paper in 2008 entitled “The missing memristor found”1. Stanley Williams and his team had been working on developing a new high speed dense memory based on a crossbar array at the nanoscale. They needed a switch that could connect overlapping crossbars, the switch they needed was a memristor.
The memristor was fabricated as follows:
They sandwiched a cube of between platinum crossbars
A region of the was auto doped by removing oxygen atoms creating a region.
These positive oxygen deficiencies can drift through the entire cube and are moved by applying an electric current.
This movement changes the resistance of the memristor.
The dopants will also remain in their position until a current is applied again. In this way the memristor has memory.
Notes: intro_HP

## Slide 9
Operation of the Memristor
Fig. a below shows the initial condition of the memristor. The oxygen vacancies act as positive dopants.
In Fig. b a positive bias is applied to the memristor and the positive charges are repelled throughout the memristor causing the boundary between the two materials to shift. In this way the resistance of the device is lowered and the device is said to be on.
In Fig. c a negative bias is applied, the positive charges are attracted to the top of the device, the resistance increases and the device is said to be off. [3]
Voltage through memristor:
RON = resistance when on,
ROFF = resistance when off,
D = length of device,
w = width of doped region
Memristance:
= average ion mobility
State Equation:
HP Memristor Equations
Notes: intro_HP

## Slide 10
Ideal
Memristor
Memristor
Voltage through memristor:
RON = resistance when on, ROFF = resistance when off
D = length of device, w = width of doped region
Memristance:
= average ion mobility
State Equation:
A memristor historically relates magnetic flux  and electric change q. This definition has been expanded to include all 2-terminal non-volatile memory devices based on resistance switching.
The general memristor is defined as:
y = input, x = state variable, u = input
The variables can have a physical interpretation.
The memristor can be either:
Charge Controlled
Flux Controlled
HP Memristor
The HP memristor is defined by the following equations:
Other Terms
Memcapacitor – the state controls the capacitance
Meminductor – the state controls the inductance
Notes: terms

## Slide 11
The following papers were used as references throughout the Toolbox. These papers are also recommended reading for anyone interested in going beyond the material presented in this Toolbox.
[1] L. Chua, “Memristor-The missing circuit element,” Circuit Theory, IEEE Transactions on, vol. 18, no. 5, pp. 507–519, 1971.
[2] L. O. Chua and S. M. Kang, “Memristive devices and systems,” Proceedings of the IEEE, vol. 64, no. 2. pp. 209–223, 1976.
[3] D. B. Strukov, G. S. Snider, D. R. Stewart, and R. S. Williams, “The missing memristor found,” Nature, vol. 453, no. 7191, pp. 80–83, May 2008.
[4] L. Chua, “Resistance switching memories are memristors,” Applied Physics A, vol. 102, no. 4, pp. 765–783 LA – English, 2011.
[5] L. O. Chua, “Nonlinear circuit foundations for nanodevices. I. The four-element torus,” Proceedings of the IEEE, vol. 91, no. 11. pp. 1830–1859, 2003.
[6] M. Di Ventra, Y. V Pershin, and L. O. Chua, “Circuit Elements With Memory: Memristors, Memcapacitors, and Meminductors,” Proceedings of the IEEE, vol. 97, no. 10. pp. 1717–1724, 2009.
[7] Y. Ho, G. M. Huang, and P. Li, “Nonvolatile memristor memory: Device characteristics and design implications,” Computer-Aided Design - Digest of Technical Papers, 2009. ICCAD 2009. IEEE/ACM International Conference on. pp. 485–490, 2009.
[8] Y. V. Pershin and M. Di Ventra, “Experimental demonstration of associative memory with memristive neural networks,” Neural networks, vol. 23, no. 7, pp. 881–886, 2009.
[9] F. Corinto and A. Ascoli, “A Boundary Condition-Based Approach to the Modeling of Memristor Nanostructures,” Circuits and Systems I: Regular Papers, IEEE Transactions on, vol. 59, no. 11. pp. 2713–2726, 2012.
[10] A. Talukdar, A. G. Radwan, and K. N. Salama, “A memristor-based third-order oscillator: beyond oscillation,” Applied Nanoscience, vol. 1, no. 3, pp. 143–145, 2011.
Notes: bib

## Slide 12
The memristor has many exciting and promising new applications. Researchers are developing neuromorphic memristor circuits, which model the brain and are able to learn. The memristor is also being used in next generation computer memory, which is not only dense, fast and non-volatile, but also is able to carry out logic operations. Another promising application is in Analogue Programmable Circuits. An investigation of the following applications is presented in this toolbox:
Memory Circuits
  Memristors are being used in circuits to create a new memory which is:
    Non-Volatile (retains its state while turned off)
    High Speed (as fast as SRAM)
    Dense ( vs. in DRAM.
  In this way memristors could potentially replace the dynamic random access memory (DRAM)
  currently used in computers.
Neuromorphic Engineering
  A circuit which can act and learn like the brain can be made possible with memristors:
    Memristors can mimic the behaviour of a synapse in the brain
    Transistors can mimic the neurons
    Crossbars can mimic the axons
  Repetitive actions reinforce memory in the brain, likewise the memristors can be “taught” by using periodic pulses to change the memristance state bit by bit.
Programmable Circuits
  The memristor enables many new effects in circuits. These effects are explored and expanded upon in this section. Novel circuits such as a non-inverting amplifier and chaotic oscillator are presented.
There are many other potential applications, which are not explored here. These include, but are not limited to, chaotic circuits, maze solving, sensing schemes, power management and information security, analogue computing, programmable analogue ICs, artificial biological systems, reconfigurable nanoelectronics, fast computations, and control systems .
The HP memristor’s structure on a crossbar architecture, as viewed on a scanning tunnelling microscope [3]
Notes: apps_intro

## Slide 13
Neuromorphic Engineering
In the nervous system a synapse is the connection between the axon of one neuron or nerve and the cell body of another nerve or neuron. This connection carries electrical and chemical signals.
An artificial synapse needs to remember its state and it needs to be able to easily change it’s state.
It has been shown in [experimental demo] that a memristor can successfully emulate a synapse in a neural network.
The artificial network showing associative memory is used to show the memristor acting as a synapse. Associative memory is the ability to associate different memories with the same fact or event. Arguably the most famous example of this are the experiments conducted on dogs by Pavlov where salivation of the dog’s mouth is set by the sight of food. Then if the sight of food is accompanied by a sound such as a buzzer over time the dog learns to associate the sound to the food and salivation can be triggered by the sound alone.
The neural network showing this behavior is shown in figure(1) where we consider the three neurons N1,N2 and N3 coupled by two memristive synapses S1, and S2
Notes: apps_intro

## Slide 14
The memristor used to emulate the synapse is described by the equations
Where α and β characterise the rate of memristance change,
VT is a threshold voltage,
R1 and R2 are limiting values and
θ(.) is a step function which causes the memristor to be bound by the limits R1 and R2.
This memristor gives a zero pinched as shown in figure(3), with
Although much is unknown about neurons, some simple brain functions can be simulated using simplified structures. Where a neuron reacts to an input voltage. If the input voltage is above a certain threshold the neuron fires a positive voltage pulse in the forward direction and a negative voltage pulse in the negative direction. It then waits a period of time and repeats. As shown in figure(2), note Vout has been shifted for clarity
α = β = 146 kΩ V-1 s-1
R1 = 675 Ω
R2 = 10 kΩ
VT=4V
V = 2 sin(ft) V

## Slide 15
Simulink – Simscape
The neural network shown in figure(1) has been re-created using Simulink, Simscape and the created memristor model.
In this circuit the neurons have been created using MATLAB functions and have been reduced to subsystems for simplicity.
In the below graphs it is clear that at first the sound of a buzzer does not cause the dog to salivate and the sight of food does. When the buzzer is sounded along with the sight of the food, the resistance of the memristor clearly falls. This is due to the reverse firing of the neuron N3. When the food is seen N3 fires a negative pulse towards both N1 and N2. If there is a buzzer sounding when this happens i.e. if N2 is firing at the same time there is now a greater voltage drop across the synapse N2, this greater voltage drop allows the memristor reduce the value of its resistance.

## Slide 16
HP Crossbar Memristor Composition
Pinched hysteresis loop and “q vs. ” for the HP memristor
The largest breakthrough in memristor development came when HP published a paper in 2008 entitled “The missing memristor found”1. Stanley Williams and his team had been working on developing a new high speed dense memory based on a crossbar array at the nanoscale. They needed a switch that could connect overlapping crossbars, the switch they needed was a memristor.
They developed the device by sandwiching a cube of between the platinum crossbars, as shown on the right. A region of the was auto doped by removing oxygen atoms creating a region. These positive oxygen deficiencies can drift through the entire cube and are moved by applying an electric current. This movement changes the resistance of the memristor. The dopants will also remain in their position until a current is applied again. In this way the memristor has memory.
The memristor’s structure on a crossbar architecture, as viewed on a scanning tunnelling microscope
Fig. a below shows the initial condition of the memristor. The oxygen vacancies act as positive dopants. In Fig. b a positive bias is applied to the memristor and the positive charges are repelled throughout the memristor causing the boundary between the two materials to shift. In this way the resistance of the device is lowered and the device is said to be on. In Fig. c a negative bias is applied, the positive charges are attracted to the top of the device, the resistance increases and the device is said to be off.
Voltage through memristor:
RON = resistance when on, ROFF = resistance when off
D = length of device, w = width of doped region
Memristance:
= average ion mobility
State Equation:
Notes: intro_HP

## Slide 17
Circuit Element | Equation | Function
Resistor |  | 
Capacitor |  | where
Inductor |  | where
Memristor |  | 
Circuit Element | Equation | Function
Resistor |  | 
Capacitor |  | 
Inductor |  | 
Memristor |  | 
There are four fundamental circuit variables:
voltage V
electric current I
electric charge q
magnetic flux 
There are three traditional passive circuit elements:
Resistor
Capacitor
Inductor
For the sake of completeness, there must also be a two-terminal circuit element which relates  and q. This element is a memristor.
“A memristor relates magnetic flux  and electric change q.”
Notes: intro_variable

## Slide 18
The Pinched Hysteresis Loop is a very important characteristic of a memristor.
The voltage of the memristor is plotted against its current.
For a memristor driven by a sinusoidal current source the plot will always be a pinched hysteresis loop.
Pinched: when
The Pinched Hysteresis Loop alone does not model a memristor.
A  – q curve or a memristance vs. state map is needed.
This plot can be used to predict the response of the system to an applied input (current or voltage).
Notes: intro_hysteresis

## Slide 19
HP Crossbar Memristor Composition[3]
Pinched hysteresis loop and
“q vs. ” for the HP memristor [3]
HP fabricated the first memristor in 2008.
They sandwiched a cube of between platinum crossbars
A region of the was auto doped by removing oxygen atoms creating a region.
These positive oxygen deficiencies can drift through the entire cube and are moved by applying an electric current.
This movement changes the resistance of the memristor.
The dopants will also remain in their position until a current is applied again. In this way the memristor has memory.
Notes: intro_HP

## Slide 20
Chua defined the memristor as the fourth fundamental circuit element, a device which relates  & q.
1971
Chua & Kang generalise the 1971 memristor as part of a broader class of “memristive systems”. They also introduced the idea of a memristive device having a state variable.
1976
Chua introduced a periodic table of all two-terminal circuit elements.
2003
HP introduced their physical memristor.
2008
Di Ventra et al. expanded memristive systems to include the memcapacitor and meminductor.
2009
Chua redefined the memristor as “all 2-terminal non-volatile memory devices based on resistance switching are memristors”.
2011
2013
Notes: intro_timeline

## Slide 21
Ideal
Memristor
Memristor
Voltage through memristor:
RON = resistance when on, ROFF = resistance when off
D = length of device, w = width of doped region
Memristance:
= average ion mobility
State Equation:
A memristor historically relates magnetic flux  and electric change q. This definition has been expanded to include all 2-terminal non-volatile memory devices based on resistance switching.
The general memristor is defined as:
y = input, x = state variable, u = input
The variables can have a physical interpretation.
The memristor can be either:
Charge Controlled
Flux Controlled
HP Memristor
The HP memristor is defined as follows:
Other Terms
Memcapacitor – the state controls the capacitance
Meminductor – the state controls the inductance
Notes: terms

## Slide 22
Memory Circuits
  Memristors are being used in circuits to create a new memory which is:
    Non-Volatile (retains its state while turned off)
    High Speed (as fast as SRAM)
    Dense ( vs. in DRAM.
  In this way memristors could potentially replace the dynamic
  random access memory (DRAM) currently used in computers.
Neuromorphic Engineering
  A circuit which can act and learn like the brain can be made possible
  with memristors:
    Memristors can mimic the behaviour of a synapse in the brain
    Transistors can mimic the neurons
    Crossbars can mimic the axons
  Repetitive actions reinforce memory in the brain, likewise the memristors can be “taught” by using periodic pulses to change the memristance state bit by bit.
Programmable Circuits
  The memristor enables many new effects in circuits. These effects are explored and expanded upon in this section. Novel circuits such as a non-inverting amplifier and chaotic oscillator are presented.
The HP memristor’s structure on a crossbar architecture, as viewed on a scanning tunnelling microscope
Notes: apps_intro